## Slide 1: Programming Your Radio
John Davis WB4QDX

## Slide 2: Decisions, Decisions
Mobile or portable/HT?
What type of radio am I programming (FM, D-STAR, Fusion, DMR, NXDN,P25)?
Front panel programming versus programing software?
How many memories do I need?

## Slide 3: Mobile vs Portable Considerations
How many memories do I need?
Can I store and select different memory loads?
How easy is it to change memories?
How do I want to organize memories (banks, areas, bands)?
Same memory order for portable and mobile

## Slide 4: Front Panel vs Programming Software
You should always know how to program directly on the radio for fast changes and quick additions in the field
Initial setup is easiest with programming software
  Requires programming cable
  Software allows easy changes and additions
  Easy to save multiple versions
  Keeps backup copies
Free and purchased programming software available

## Slide 5: Basic Programming for FM
What I need to know for programming
  Output frequency of repeater
  Duplex direction (+ or -)
  Offset (usually 600KHz for 2m/5 MHz for 70cm)
  Tone frequency (Hz)
  Tone on TX or tone squelch (TSQ)

## Slide 6: Basic Programming for D-STAR
What I need to know for programming
  Output frequency of repeater
  Duplex direction (+ or -)
  Offset (usually 600KHz for 2m/5 MHz for 70cm)
  Tone frequency (Hz)
  Tone on TX or tone squelch (TSQ)
Plus
  My callsign
  Local repeater callsign
  Module (B for UHF, C for VHF)
Enter own callsign
Turn on GPS
Nearest Repeater
OR

## Slide 7: Basic Programming for Fusion
What I need to know for programming
  Output frequency of repeater
  Duplex direction (+ or -)
  Offset (usually 600KHz for 2m/5 MHz for 70cm)
  Tone frequency (Hz) for FM
  Tone on TX or tone squelch (TSQ) for FM
Plus
  Change mode to DN or DW (digital narrow or wide) for C4FM digital mode

## Slide 8: Basic Programming for DMR
What I need to know for programming
  Output frequency of repeater
  Duplex direction (+ or -)
  Offset (usually 600KHz for 2m/5 MHz for 70cm)
  Tone frequency (Hz)
  Tone on TX or tone squelch (TSQ)
Plus
  Color code
  Talkgroup number by repeater
  Create Zone

## Slide 9: Programming Software
Free software (still need programming cable)
  Chirp (available for most radios)
  Some manufacturers (usually for specific models)
Purchased Software
  RT Systems
    reasonably priced
    allows easy copying from one radio to another
    Sells programming cables