## Slide 1: Ridgid Pro Organizer toolbox & Cart transformation to vhf/uhf Radio go-box Set

## Slide 2: Design objectives
Implement an amateur radio go-box suitable for the following use cases:
Portable deployment
  Self-contained system
  Manageable weight and mobility
  Rapidly deployable with minimum setup time
  Emergency power solution safe for indoor use
  Digital operations (e.g., Winlink messaging and D-Star)
Home radio shack
  Rapid transition from portable use to base station use

## Slide 3: Basic Design questions
Case choice
  Rack system (e.g., 4U rack travel case)
  Pelican case solution
  Other case types (e.g., RIDGID)
Integrated and/or external power supply?
  Space / weight / ease-of-use
  Battery or power supply unit
Closed or open case operation?
  Thermal considerations
  Moisture considerations

## Slide 4: RIDGID Tool Boxes
Heavy-duty construction
Stackable, lockable system
Moisture / dust resistant
Relative cost lower compared with other options (e.g., Pelican)

## Slide 5: N7GRB Go-BOX Basic features
RIDGID Pro Organizer case & Tool Cart
  Provides dust and moisture protection during transit to/from deployment site
ICOM ID-5100 Transceiver
  Dual band VHF / UHF with D-Star Digital voice/data
External connections for power, antenna and microphone
Console with power meter, car style 12v DC receptacle and USB charge ports
20 amp continuous/ 23 amp surge 13.8v DC power supply
Storage area
  Signalink, A/B switch, ICOM control head and associated cables

## Slide 6: Component wiring plan
Simple DPDT ON-OFF-ON switch selects power source
Rocker switches control power to accessories
Easy access fuse protection on DC circuits
Standard Anderson Power Pole connection (Powerwerx port) to external DC power source (battery box)

## Slide 7: Power Distribution Control
Power mgmt console
Car style 12v DC receptacle
USB charge ports
Fuse access
Power monitoring
Led rocker switches
Don’t Look Under the Hood
Automotive style crimp connections
WAGO Lever Nuts
WAGO Lever Nuts
5 Conductor Compact Connectors
Up to 12 AWG
20A 600V UL rating (IEC/EN 32A/450V)

## Slide 8: Some AssEMbly Required …
RIDGID Pro Organizer
  Inside lid, parts buckets and dividers removable
Parts and more parts … never enough

## Slide 9: Foundation
Wood base board
  Firm attachment of PSU and radio to base board
  Base board attached to case bottom

## Slide 10: External Connections
Mic and Antenna
(right side)
A/C and DC Input
(left rear corner)

## Slide 11: Battery & Storage Box
Bioenno 30 AH battery
  Integrated over current / low voltage protection
  Shock pad under battery
MFJ-4416C Battery Booster
  25 Amps ICAS 30A peak
  13.8 Volts at 9-13.8 volts input

## Slide 12: Battery & Storage Box
Master power switch
  Lock-out protection feature
Powerwerx Power Pole ports
  Charge port
  Power port

## Slide 13: Deployed
Normal operation with lid open for natural air ventilation
Lid has:
  Whiteboard for notation of situation info
  LED lighting
Large digital clock
ICOM ID-5100 control head mounted on articulating stand
Removable storage box holds Signalink, A/B switch and associated cables

## Slide 14: Deployed
Gwinnett Sheriff Jail Break Run
American Red Cross Communications Exercise

## Slide 15: Antenna
Slim Jim dual-band VHF / UHF antenna
Slim Jim suspended between PVC pipe arms attached to lightweight collapsible mast
Mast also supports HF Alpha Antenna

## Slide 16: N7GRB IC-7100 GO-Box Prototype
RIDGID Tool Box and a Little PVC

## Slide 17: George Zafiropoulos KJ6VU IC-7100 RIDGID Go-Box
Design approach
  External power source
  Closed case with powered ventilation

## Slide 18: K6CPO RIDGID Based Go-Box Set johnwright.smugmug.com

## Slide 19: Ridgid Tool Cart – Pvc go-box
Fits in RIDGID Tool Cart
Dual radios VHF/UHF and HF with power supply

## Slide 20
Thank You!