## Slide 1: Talking Through The Birds
Ruth Willet, KM4LAO
August 10, 2021

## Slide 2: Presentation Scope
Types of Satellites
Low Cost OTA
Satellite Pass Checklist
Connecting Off Satellites
Awards

## Slide 3: From Sputnik I to OSCAR Satellites
https://www.nationalgeographic.com/science/2018/10/news-sputnik-world-space-week-soviet-union-russia/
https://amsat-uk.org/2018/01/26/ao-92-open-for-amateur-radio-use/

## Slide 4: AMSAT
https://www.amsat.org/

## Slide 6: Orbital Period = Time to complete one trip around the earth
All current satellites in LEO
Orbital period: 88-127 minutes

## Slide 7: QSOs occur when we are in a satellite’s footprint
Footprint varies per pass due to earth’s rotation
One satellite can have ~8 passes per day at varying times & elevations

## Slide 8
Types of Satellites
Digisats
FM Satellites
Linear Transponders

## Slide 9: Digisats
Digital Modes
2m Simplex
Equipment: 1 HT & Directional Antenna

## Slide 10: Digipeater Available on the ISS

## Slide 11: FM Satellites
SO-50: 145.850 MHz
SO-50: 145.850 MHz
5 active FM satellites
  Some only active on a schedule
Orbiting Repeaters
Cross-Band Repeaters
  U/V: TX on 2m, RX on 70cm
  V/U: TX on 70cm, RX on 2m
Transmit = uplink,
Receive = downlink
CTCSS Tone Required

## Slide 12: SO-50
Mode U/V
  TX on 2m, RX on 70cm
Mode V/U
  TX on 70cm, RX on 2cm
AO-91

## Slide 13: FM Satellites are great to start with and fun to operate on!

## Slide 14: Linear Transponders
Cross-band QSOs
USB, LSB, CW, Digital
Built for entire range of frequencies
  A satellite passband
Passbands range from 20-100 kHz

## Slide 15: FM Repeater vs Linear Transponder

## Slide 16: Types of Linear Satellites
Non Inverting
TX USB High End Passband
RX USB High End Passband
Inverting
TX LSB Low End Passband
RX USB High End Passband
Courtesy of Emily, W0EEC

## Slide 17: Linear Transponders are an upgrade from FM sats due to generally greater footprints and more space for QSOs in the passband

## Slide 18: Why I Like Satellites
Bounce signals of moving target
Talk anywhere in constantly changing footprint
Multi-task to TX/RX with multiple radios and track satellite
Communicate accurately at fast pace
Doppler Effect challenge

## Slide 19: Doppler Effect: A characteristic of a moving signal

## Slide 20: Doppler Effect on SO-50

## Slide 21: Doppler Effect on Linear Transponders

## Slide 22: Situational Awareness is Imperative
FM Pass: Don’t call CQ
Linear pass: Spread out in passband, free to call CQ

## Slide 23: Satellites Gear Checklist
Item | Options | Price
Directional Antenna | Yagi - Arrow, Elk | $152
VHF/UHF Radios | Any brand | $25 - $400 Entry level
Low Loss Coax | RG58, Wireman #118, HRO, Etc | $5
SMA to BNC Connectors | Multiple | $6
Duplexer (optional) | Arrow, MFJ | $34
Satellite Pass Prediction Software | Multiple | Free
Grid Square Prediction | Multiple | Free
Compass | Physical compass, phone app | Free
Voice Recorder | Separate recorder, phone app | $45
 | Total Cost: | $250 - $600

## Slide 24: Directional Antenna: Elk or Arrow Handheld

## Slide 25: VHF/UHF Radios
Handhelds or base station
  Icom
  Kenwood
  Yaesu
  Baofeng

## Slide 26: Operating Full Duplex is CRITICAL

## Slide 27: Linear Satellites: Radios with SSB/CW/Digital Capability on VHF/UHF
Yaesu FT817 or FT818
Yaesu FT-847 (full duplex)
Icom 7300 (full duplex)
Icom 910
Icom 705
Mix and match to get full duplex as needed

## Slide 28: Low Loss Coax, Connectors, Duplexer as needed
Low loss coax like RG58, Wireman #118, HRO Equivalent
Standardize with BNC Connectors
One Radio
  Duplexer connects antenna elements to radio
Two Radios
  Duplexer + coax
  2 lengths of coax

## Slide 29: Maidenhead Grids
First two letters :10 degree by 20 degree fields
Sub fields, 00-99 per letter combination: 1 degree latitude by 2 degrees longitude

## Slide 30: Determining Your Grid Square

## Slide 31: Pass Prediction - AMSAT: https://www.amsat.org/track/index.php

## Slide 32: Pass Prediction N2YO: https://www.n2yo.com/

## Slide 33: Pass Prediction Software List
AMSAT: https://www.amsat.org/track/index.php
N2YO: https://www.n2yo.com/
Gpredict: http://gpredict.oz9aec.net/
MacDoppler: https://www.dogparksoftware.com/MacDoppler.html
GoSatWatch (iPhone)
AmsatDroid (Android)
ISS Detector (Both)

## Slide 34: Pass Prediction – iPhone Apps

## Slide 35: Compass

## Slide 36: Voice Recorder

## Slide 37: Logging Satellite Passes
https://twitter.com/WD9EWK/status/976839455658176513
N3FJP
TQSL
https://www.magicbug.co.uk/cloudlog/

## Slide 38: What do we talk about?
Potential QSO on a busy pass
KX9X, this is KM4LAO
KM4LAO, this is KX9X, EN50
QSL Sean, I’m in EM79!
QSL, Ruth

## Slide 39: Home Grid Stations and Rovers
DD1US
Kylee, KE0WPA

## Slide 40: Satellite Pass Checklist Part 1- Pre Pass
Choose a satellite and pass to operate on
Determine operating location based on direction and elevation of pass
Gather equipment and charge radios
Make sure FM frequencies are programmed in radio memory

## Slide 41: Satellite Pass Checklist Part 2 - Pre Pass
Walk/Drive to operating site
Assemble antenna and connect radios
Mark AOS, Peak Elevation, and LOS
Start recording, state date and time, grid square, callsign, and satellite

## Slide 42: Satellite Pass Checklist Part 3 – Mid Pass
Track where the satellite should until you hear it
Listen until you get the rhythm of pass
  Listen for other rovers, special events, try to understand who is on the air
Call someone directly or just transmit your callsign and gridsquare
Repeat for the entire pass

## Slide 43: Satellite Pass Checklist Part 4 – Post Pass
Transcribe recording
Log contacts
Upload to LOTW for confirmation and award credit
Send QSL cards as desired

## Slide 44: Successful Contact

## Slide 46: Satellite Linear Tips
Use KE0PBR Frequency List
Track satellite using app
  Often most beneficial to find the beacon first
Pick downlink or uplink on 2m, set that freq on radio, and lock it
Scroll uplink or uplink to corresponding 70cm frequency and be prepared to adjust for Doppler
Find yourself on the passband and try not to step on others
  Soft whistles help sometimes, or “testing 1,2,3”
  Operators know it can be hard to find yourself, so be patient
  If you don’t find yourself, go back to the starting frequency and slowly change the freq until you do
Start calling CQ to make contacts!

## Slide 47: Satellites Linear Frequencies

## Slide 48: Linear Satellite Pass Video
https://youtu.be/cwtmP1sDL9g?t=115

## Slide 49: Earning Standard Awards

## Slide 50: Earning Customized Awards

## Slide 51: AMSAT Distance Records

## Slide 52: AMSAT Rover Award

## Slide 54: Connections On The Air: AMSAT Net

## Slide 55: Twitter for Hams

## Slide 56: SatMatch

## Slide 57: GridMaster Heat Map

## Slide 58: General Links
AMSAT Homepage
  https://www.amsat.org/
Paul, KE0PBR’s frequency Excel spreadsheet
  https://ke0pbr.wordpress.com/2018/12/31/my-frequency-cheat-sheet/
FM Satellite Frequency Summary
  https://www.amsat.org/fm-satellite-frequency-summary/
OSCAR Satellite Status Page
  https://www.amsat.org/status/
AMSAT UK
  https://amsat-uk.org/

## Slide 59: Satellites are…
Accessible
Affordable
Fantastically Fun
Challenging
Connecting with Community
Always Providing Learning Opportunities
... for everyone!

## Slide 60: Questions?